HARTWCK.GIF and HARTWCK2.GIF (1024x768 and 800x600)

 This scan shows another "bargin basement" coil built by Dave
 Hartwick. The secondary coil is wound with enamel covered magnet
 wire on a six inch diameter thin wall PVC plastic drain pipe.
 The plastic pipe was sealed with several coats of polyurethane
 before the coil was wound, and the coil was coated again with
 several coats of sealer over the windings to reduce corona loss.
 The discharge terminal is an inverted stainless steel mixing
 bowl. The discharger is taped to the top of the secondary with
 several turns of black electrical friction tape. This taping
 also helps to prevent corona loss and premature breakout from
 the tightly rounded lip of the bowl.

 The primary coil is about six turns of three-wire electrical
 extension cord that has all three conductors fused at the ends.
 The six turn primary is a "flat pancake" (Archimedes spiral)
 wound on a coil form constructed of plexiglas strips mounted in
 a simple hardwood frame. Pegs cut from wooden dowels are plugged
 into holes drilled in the plexiglas strips to act as spacers be-
 tween primary turns.

 The spark gap is a cylinder static gap constructed from 14, two
 inch long sections of 1-inch diameter hard copper water pipe
 mounted inside of a short length of standard six-inch PVC drain
 pipe. Air flow through the pipe is provided by a small muffin fan.
 Only seven gaps are used, with the spacing between electrodes set
 at about .030 inches. This cylinder gap is mounted horizontally
 instead of the usual vertical construction. A plastic drinking
 cup and some foam insulation have been crammed into the spark
 gap to choke the airflow through the center of the unit and
 increase the speed and amount of airflow between the electrodes.

 The capacitor used in this coil project is a small homemade
 plastic/foil capacitor constructed using a small plate of plexi-
 glas. The designer/builder stated to me that he was not happy
 with the capacitor performance, having seen flashovers and
 heavy corona losses from the uninsulated plates. The actual
 capacitor can be seen directly behind the base of the secondary.
 It is a long foil covered rectangle.

 The power supply pictured here is a single 12 kV 30 mA neon sign
 transformer.

 One little note that I pointed out the the builder: the primary
 coil form is sitting on top of a formica table. The section of
 the table top visible in the photo (and the scan) is edged with
 a strip of heavy aluminum. I suspected that this strip goes
 completely around the table top and forms a single shorted turn
 "square" coil! I picked up the phone an called. Being familiar
 with this type of table construction, I asked if there was a
 tiny gap where the strip of aluminum edging (the single square
 turn) met. I waited a moment as the builder crawled under the
 table to discover the an arc had been forming at this location
 and the the pressboard tabletop had been carbonized at this
 location!

 This coil was designed, built, and operated by: Dave Hartwick
 191 Highland Rd., Chambersburg, PA  17201  USA