PICG1024.GIF and PICG800.GIF

 This is a scan of one of my first coils built some years ago.
 The secondary coil form is five inch diameter plexiglas that
 I ordered specifically for this project. The winding is 20
 inches long and consists of about 750 turns #22 magnet wire.
 The bare coil resonates at about 400 kHz, I would guess the
 coil with sphere discharger resonates at about 370 kHz. The
 sphere discharger was the top of a large a flag pole, though
 I have no idea how it found it's way down and on top of my coil.

 The primary coil used was 3/8 inch soft copper refrigerator
 tubing, about 8 turns, wound in small inverse conical section.
 The tank circuit capacitance was a commercially made .01 micro-
 farad oil capacitor rated at 20,000 volts that I found surplus.
 The power supply was two 12 kV 30 mA neon sign transformers
 wired in parallel. The spark gap was a simple setup using two
 brass bolt. Discharge length was a solid 18 inches.

 This photo is an excellent example of the corona losses that
 occur when using spherical dischargers in general, or any
 discharger that does not have a large enough diameter in
 relation to the coil form. Heavy corona and sparks issue out
 of the top turns of the coil which is not good.

 System designed, built, and operated by: Richard T. Quick II
 10028 Manchester Rd., Suite 253, Glendale, MO  63122 USA