PICM1024.GIF and PICM800.GIF

 These are two scans (1024x768 & 800x600) of a small Tesla
 Magnifier operating at 720 VA producing discharge and corona
 of about a 18 inches in length.

 The extra coil is a six inch diameter sealed PVC coil form
 wound with about 900 turns of #21 magnet wire. The winding
 length is about 28 inches and the coil is topped with a 20 inch
 toriod discharger. This coil is standing on a five gallon
 plastic bucket. This extra coil is resonating without a primary
 or tank circuit inductively coupled to it. The extra coil is
 base fed by a transmission line that originates at the top of
 the system secondary coil to the left.

 The transmission line used here is simply a clip lead and a
 short length of magnet wire from the base of the extra coil.
 This system is less than efficient, but I have found that a
 high impedance in the transmission line promotes corona loss
 which can be easily photographed. Even with the lack of back-
 ground detail there should be no doubt how the energy is
 introduced into this freely resonating coil.

 The power supply used is two 12 kV 30 mA neon sign transformers
 wired in parallel. The spark gap used was small rotary gap. The
 tank circuit capacitance consists of two, .02 microfarad, home-
 made rolled capacitors in series for .01 microfarads system
 capacitance rated at about 20,000 AC volts pulse.

 System was designed, built, and operated by Richard T. Quick II
 10028 Manchester Rd., Suite 253, Glendale, MO  63122  USA