Here I am standing behind the two 25 KVA pole pigs while drawing
about 6 inches of arc from the high voltage terminals. The low
voltage windings are wired in parallel for 0-280 volts inputs.
The cores and cans of the two pigs are commoned and grounded to
the RF ground. The two HV windings are in series. Static input
voltage is 100 volts, the energy expended in the arc is ~2500
watts.

Richard Quick